## Slide 1: A Real Time Application to Identify Alcoholics from ECG Signals
Akarsh N Kolekar (1PI13EC009) Guide: Dr. b Niranjana Krupa
Apoorv Vatsal (1PI13EC017)
Rakshith Vishwanatha (1PI13EC075)

## Slide 2: Work Done By First Review
RAKSHITH
  Time domain feature extraction
  Non linear feature extraction
APOORV
  Raspberry pi setup
  Frequency domain feature extraction
AKARSH
  Circuit design/simulation
  Introduction to ELM classifier

## Slide 3: Work Done By Second Review
RAKSHITH
  Implemented SVM Classifier on MATLAB
  Started Porting Code onto Python
  Started work on Circuit and interface with Raspberry-Pi
APOORV
  Converted all MATLAB toolbox operations to MATLAB scripts
  Worked on AR Modelling. Started work on ARX.
  Started work on Circuit and interface with Raspberry-Pi
AKARSH
  Implemented ELM Classifier on MATLAB
  Implemented ELM Classifier on Python
  Started work on Circuit and interface with Raspberry-Pi

## Slide 4: Work Done Since Last Review
RAKSHITH
  Trained and tested SVM for unbiased dataset with crossvalind()
    80% - 90% accuracy
    Earlier, biasing and self-written k-fold code gave 98% accuracy)
  Feature reduction techniques -- PCA and Combinational Selection
    PCA could reduce 23 features to just 2 dimensions with 80% accuracy
    Realised that PCA was not required to select features
    But it showed high correlation in features being extracted – can expect good reduction though comnk()
    Combination Selection done using combnk()
    Number of essential features was reduced to just 17 features
    Accuracy retained at 88%

## Slide 5: Work Done Since Last Review
RAKSHITH
  Completed porting time domain, non-linear feature extraction MATLAB code to Python
  Worked on designing filters for ECG sensor
    LPF and HPF range for filters studied and implemented
    Notch filter designed and soldered

## Slide 6: Circuit – Design
Original circuit had just the instrument amplifier and LPF
  We got 50 Hz signals with superimposed ECG signal
Decided to remove 50Hz using a Twin T notch filter
  Fc = 50Hc, Q = 0.75
Met Dr. Maruthy to discuss more about circuit design and placement of leads of the sensor
  Also go additional inputs about using Audacity for off-site filtering

## Slide 7: Circuit – Design
Clean 50 Hz signal
Original Circuit
ECG signal superimposed on 50Hz

## Slide 8: Circuit – Design
New circuit tried on breadboard
  Promising results (signal spikes every 1.2s) but unstable
  Implementing soldered version

## Slide 9: Alternative Sensor
As an alternative, we have used an AD8238 ECG sensor to obtain ECG signals on the CRO
Worked on R-pi to sample signals at required 1KHz
  Sampled signal is stored as a CSV
Output on CRO
AD8232 with ECG sticky pads

## Slide 10: Sensor Interface with R-pi
Interface diagram of Analog sensor with MCP 3008 ADC
1kHz sampling required without being able to find actual sampling rate of the DAC – timer() class

## Slide 11
Sensor Interface with R-pi
CSV file generated from the sampled and digitized analog signal
Code to sample at 1kHz

## Slide 12: Work Done Since Last Review
APOORV
Worked on ARX modeling of ECG signals
  Coefficients were obtained which will be form as additional features for classifier
Interfaced sensor with Raspberry-Pi to obtain CSV file at correct sampling rate
Working on implementing ECG sensor and verifying operation of AD8232

## Slide 13
Modelling of Signals
APOORV
  AR Model Structure:
  ARX Model Structure:

## Slide 14
Work Done
System Identification toolbox

## Slide 15: Work Done

## Slide 16: Work Done Since Last Review
AKARSH
  Applied self-written Gaussian Kernel to dataset.
  Feature dimensions increased from 23 to 67 (i.e., number of samples)
  No increase in accuracy observed for classifier with Kernel use (accuracy remained at ~70%) for K-fold cross validation with k=8.

## Slide 17: Work Done Since Last Review
AKARSH
  Implemented Kernel function in Python and MATLAB
    Tested Kernel for varying values of variance (Sigma) from 0.001 to 100.
    Highest accuracy was obtained for Sigma=1.111
  Understood Meta Cognitive Learning Algorithm for an Extreme Learning Machine Classifier by studying a paper.
  Worked on implementing ECG sensor circuit and verifying operation of AD8232 Sensor

## Slide 18: MetaCognitive ELM
The architecture of McELM is not fixed a priori
Network is built during the training process
Meta-Cognitive component of McELM has a self regulatory learning mechanism that decides what-to-learn, when-to-learn and how-to-learn
Samples from training set are presented one by one and meta cognitive component chooses suitable learning strategies for the sample
Learning strategies include: deleting sample, adding neuron, updating output weights, or reserving samples for future use

## Slide 19: MetaCognitive ELM
Neurons in Hidden layer employ q-Gaussian activation function
Adding a neuron: Centres chosen based on the sample, width of Gaussian function chosen randomly
Output weights estimation: Least square estimate using hinge loss error function
Why Hinge Loss Error Function? It facilitates prediction of posterior probabilities better than mean square error.

## Slide 20: What we expect from McELM
Reduced number of hidden layer neurons
Better accuracy
Lesser overfitting
Lesser computational effort
Improvement in generalization capability

## Slide 21: TARGETS FOR THE NEXT REVIEW
RAKSHITH
  Implement Meta-Cognitive ELM
  Implement Classifier section of SVM code in Python
APOORV
  Remove dependence on System Identification toolbox and convert everything to command line codes
  ARX modeling coefficients to be calculated for all samples and consolidated into a single csv file, one for alcoholics and other for non-alcoholics
  Port the frequency domain feature extraction MATLAB code to Python
  Integrate hardware and python code on the Raspberry Pi to make a complete system
AKARSH
  Implement Meta-Cognitive ELM

## Slide 22: Literature Survey
Pico Technoology, “Electrocardiogram (ECG) circuit for use with oscilloscopes”. [Online] Available: https://www.picotech.com/library/application-note/electrocardiogram-ecg-circuit-for-use-with-oscilloscopes
Lv Jinhua and Xu Yanyi, “Circuit Design for Front-End Electrocardiograph”, International Journal of Multimedia and Ubiquitous Engineering Vol.11, No.5 (2016), pp.345-354
Ajay Bharadwaj and Umanath Kamath, Cypress Semiconductor Corp., “Techniques for accurate ECG signal processing” [Online] Available: http://www.eetimes.com/document.asp?doc_id=1278571
NTHU, “ECG Circuits, Signal Sampling and Digitalization” [Online] Available: https://www.google.co.in/url?sa=t&rct=j&q=&esrc=s&source=web&cd=1&cad=rja&uact=8&ved=0ahUKEwins5jwg43TAhWCq48KHcxPAysQFgggMAA&url=http%3A%2F%2Flms.nthu.edu.tw%2Fsys%2Fread_attach.php%3Fid%3D692351&usg=AFQjCNFJqOwwhxZZG0FP1yQNMuNpHBV73Q&sig2=e_-aLgXrLbFMIB-XhTd2Kg

## Slide 23: Literature Survey
L. Ljung,“System identification toolbox,” The Matlab user’s guide, 2012. [Online] Available: http://radio.feld.cvut.cz/matlab/pdf_doc/ident/ident.pdf
Hong He, Xiaowen Yan and Wei Wei, “Meridian ECG Information Transmission System Modeling Using NARX Neural Network” ,IEEE/ACIS 15th International Conference on Computer and Information Science (ICIS), 2016. [Online] Available:http://ieeexplore.ieee.org/document/7550775/
R. Savitha, S. Suresh, H.J. Kim, “A Meta-Cognitive Learning Algorithm for an Extreme Learning Machine Classifier” Cognitive Computation, vol. 6, pp. 253-263, 2014.

## Slide 24: TIMELINE
On schedule as per expected timeline