## Slide 1: A Real Time Application to Identify Alcoholics from ECG Signals
Akarsh N Kolekar (1PI13EC009) Guide: Dr. b Niranjana Krupa
Apoorv Vatsal (1PI13EC017)
Rakshith Vishwanatha (1PI13EC075)

## Slide 2: STATUS – since synopsis (21st Jan)
Raspberry Pi
Feature Extraction
Circuit Simulation
Classifier

## Slide 3: RASPBERRY PI
Installed the OS
Enabled ssh to accessed terminal
Set static IP – cmdline.txt was used – IP and netmask provided

## Slide 4: FEATURE EXTRATION
Time domain
Frequency domain
Non-linear techniques

## Slide 5: TIME DOMAIN
  Based on PSD of generic ECG signal, an IIR HPF filter was designed to remove the low frequency baseline wandering

## Slide 6: TIME DOMAIN

## Slide 7: FREQUENCY DOMAIN
Techniques possible:
  Fourier Analysis – time information is lost
  Short Time Fourier Analysis – limited precision based on window size
  Wavelet Transform

## Slide 8: WHY WAVELET
Contains both frequency and time domain information
Splits parent signal to different freq components, allowing isolation of low frequency baseline wandering
R peak detection and RR interval calculation done

## Slide 9: GRAPHS – MATLAB WAVELET TOOLBOX

## Slide 10
Wavelet Toolbox of Matlab
Daubechies (dB5) wavelet considered as mother wavelet
Scale level used was 7

## Slide 11: GRAPHS FOR ECG SAMPLE – MATLAB
Base line wandering removed using Wavelet transform

## Slide 12: GRAPHS – PYTHON
De-trending the signal and RR peak detection was also implemented on Python
Notes: Module used : biosppy,numpy and matplotlib

## Slide 13: PSD OF RR INTERVAL SERIES

## Slide 14: NON-LINEAR: POINCARE PLOT

## Slide 15: NON LINEAR: APPROX & SAMPLE ENTROPY

## Slide 16: FEATURES EXTRACTED
Time Domain
  mean_rr, STD_rr, mean_hr, STD_hr, RMS_rr, rr_50, p_rr_50
Frequency Domain
  pk_freq, abs_pow, rel_pow, norm_pow, LF_pow/HF_pow
Non-Linear
  Poincare plot’s SD, ApEn, SamEn

## Slide 17: FEATURES WHICH CAN BE EXTRACTED
Based on need as per classifier performance, following features can be added:
  Time Domain
    rr_hist, baseline_width_rr_hist
  Frequency Domain
    Sample Entropy – different ‘r’, ‘m’
  Non-linear
    DFA (Detrended Fluctuation Analysis), RPA (Recurrence Plot Analysis)

## Slide 18: HARDWARE/CIRCUIT
Studied various circuit designs available to acquire ECG Signals
Met senior who had designed the circuit for his device
Simulated circuits designed using sample base designs provided in AD620 Data-sheet, as well as circuits used by senior.
Made modifications to circuit design as per requirements and issues faced.

## Slide 19
Simulated on MultiSim. The leg circuit to provide virtual ground did not work as expected.
Erroneous outputs resulted in abandoning the circuit for other options.
ECG CIRCUIT FROM AD620 DATASHEET

## Slide 20: MODIFIED CIRCUIT
The circuit designed by senior was interfaced with a bluetooth module. We will not be using bluetooth.
It also contained an integrator circuit in the second stage. We did not understand the use of such a part of the circuit, and resulted in erroneous output.
Certain values of components(Resistors and Capacitors) were changed in order to obtain the necessary gain required.

## Slide 21: OVERALL IDEA OF CIRCUIT
Virtual ground:
  To provide a reference with respect to which the voltage at the fingertips can be measured.
  The virtual ground will be provided to the thumb, so that the device can be hand held.
Instrumentation amplifier:
  Used to measure the differential voltage between the two fingertips on both hands with respect to the virtual ground(thumb).
  This stage provides most of the amplification.
Regular amp:
  To provide secondary amplification after the instrumentation amplifier, i.e., to spread out the gains.

## Slide 22: MODIFIED CIRCUIT
RG=249Ohm
G1=200
Voffset1=3.167mV
Voffset2=45.8mV
G2=5

## Slide 23: CIRCUIT DESIGN FOR R-PI COMPATIBILITY
Max Differential I/P voltage=2.7mV
Leads to saturated output of 2.78V
Max I/P to each electrode=10.2mV
R-Pi does not have analog I/Ps
External ADC required(MPC3008)
10 bit ADC[0-1023]
R-Pi can take I/P from 0-3.3V
Resolution of R-Pi=3.22mV
If we increase supply voltage from 5V, we can increase range of I/P

## Slide 24: CLASSIFIER
Found ELM documentation by developer.
Currently understanding ELM in order to implement it.
Algorithm:
W1 is the matrix of input-to-hidden-layer weights, σ is some activation function
W2 is the matrix of hidden-to-output-layer weights
Fill W1 with Gaussian random noise;
Estimate W2 by least-squares fit to a matrix of response variables Y, computed using the pseudoinverse, given a design matrix X:
Need to explore SVM
Additional classifers to explore
  RVM
  parametric and non-parametric models, System Identification

## Slide 25: WORK DONE
RAKSHITH
  Time domain feature extraction
  Non linear feature extraction
APOORV
  Raspberry pi setup
  Frequency domain feature extraction
AKARSH
  Circuit design/simulation
  Introduction to ELM classifier

## Slide 26: TIMELINE
On schedule as per expected timeline

## Slide 27: TARGETS FOR THE NEXT REVIEW
RAKSHITH
  Consolidate Features to CSV file
  Explore SVM as a classifier
  Construct and test circuit on breadboard
APOORV
  Port all MATLAB code to R-PI to remove toolbox dependency
  Construct and test circuit on breadboard
AKARSH
  Train ELM classifier for consolidated features file
  Construct and test circuit on breadboard